| Place tick in applicable box | Ok | Action |
| --- | --- | --- |
| 2-3 weeks before the event |
| Track measurements, markings and levels |
| Verify the facility survey report if Level 3 event or above |  |  |
| Check Track survey to see if track measured with/w’out curb |  |  |
| Verify track curb all around the track |  |  |
| Check all races can be held whilst the curb is in place. |  |  |
| Check track markings and colours |  |  |
| Event programming and facilities |
| Confirm with the facility the list of events taking place. |  |  |
| Review any potential safety issues re: layout v timetable |  |  |
| Check if there is a reqt for concurrent pools in events |  |  |
| Confirm the timetable of events. |  |  |
| Equipment |
| Age-Groups taking part to determine implement weights |  |  |
| Equipment lists for track and for each field event. |  |  |
| What equipment you need to bring. (E.g. Photo finish, EDM). |  |  |
| Space and available equipment for checking implements. |  |  |

| Place tick in applicable box | Ok | Action |
| --- | --- | --- |
| Confirm power supply is available: PA, photofinish etc) |  |  |
| Confirm who will set up events (hurdles/starting blocks etc) |  |  |
| Space for event administration. (officials room, photo finish) |  |  |
| Space and PA equipment for announcers. |  |  |
| Results production: Printing, photocopying and display space |  |  |
| Check location of lap counters, timekeepers & judges stands |  |  |
| Check the location and number of computers for photo finish |  |  |
| Field Events |
| Determine who will layout the field & available equipment |  |  |
| Check status and condition of all equipment and bars |  |  |
| Verify circle diameters/depths, runway widths and lengths. |  |  |
| Check that circles and runways are clean, dry & in good repair |  |  |
| Check sector, circles, runways & circulation areas for hazards. |  |  |
| PV/HJ: Check landing areas are secured & in good condition |  |  |
| PV/HJ: Check that uprights are available/not bent or damaged |  |  |
| SP: Check stop board to ensure it is tightly held in the concrete |  |  |

| Place tick in applicable box | Ok | Action |
| --- | --- | --- |
| HT/DT: Check concentric ring is properly installed |  |  |
| HT/DT: Check the cage opening and position of the gates |  |  |
| HT/DT: Check condition of cage and netting for holes & gap |  |  |
| LJ/TJ: Put down any additional horizontal take off boards |  |  |
| LJ/TJ: Check boards to see if they need repair or levelling |  |  |
| LJ/TJ: Check that sand is even and level with take-off board |  |  |
| General |
| Likely number of spectators (Will this require stewards?) |  |  |
| Will any temporary barriers be required? |  |  |
| Access arrangements. (Athletes, officials, spectators. |  |  |
| Any need for allocated seating. (e.g. timekeepers?) |  |  |
| Catering requirements. Spectators, athletes, officials |  |  |
| Parking for competitors, spectators, officials, VIPs |  |  |
| Call room location (if required) |  |  |
| Toilets and changing for athletes. Toilets for spectators. |  |  |
| Confirm venue safety and evacuation procedures. |  |  |

| Place tick in applicable box | Ok | Action |
| --- | --- | --- |
| On the day of the event |
| General |
| Arrive at least 90mins before the first scheduled event |  |  |
| Conduct a safety walk round of the facility |  |  |
| Hold a team briefing to discuss any timetable/safety issues |  |  |
| S’Chase: Clean water jump before filling with water |  |  |
| Check sector, circles, runways & circulation areas for hazards. |  |  |
| Check to make sure that you have all required equipment |  |  |
| Use barriers/taping to restrict access to runways/field events |  |  |
| Make sure all equipment is present and in good condition |  |  |
| Track Events |
| Check location of wind gauge for first event |  |  |
| Deploy cones on a track without/missing curb |  |  |
| Place tick in applicable box | Ok | Action |
| Locate photo finish |  |  |
| Mark 800m break line |  |  |
| Check hurdle heights |  |  |
| Field Events |
| Check the sector layout/alignment |  |  |
| Check that circles and runways are clean, dry & in good repair |  |  |
| PV/HJ: Check that uprights are in good condition and set right |  |  |
| PV/HJ: Check the length and sag of crossbars |  |  |
| PV/HJ: Check location & condition of landing areas |  |  |
| SP: Check stop board to ensure it is tightly held in the concrete |  |  |
| HT/DT: Check concentric ring is properly installed |  |  |
| HT/DT: Check the cage opening and position of the gates |  |  |
| HT/DT: Check condition of cage and netting for holes & gap |  |  |
| Place tick in applicable box | Ok | Action |
| LJ/TJ: Install the long and triple jump boards. |  |  |
| LJ/TJ: Check boards to see if they need repair or levelling |  |  |
| LJ/TJ: Check that sand is even and level with take-off board |  |  |
| LJ/TJ: Loosen sand in the landing areas & moisten |  |  |
| Post Event |
| HT/DT: Repair any holes made by throwing implements |  |  |
| HT/DT: Inspect sprinkler heads for any damage |  |  |
| LJ/TJ: Sweep sand back into the landing area |  |  |
| LJ/TJ: Replace the covers over landing areas and jumping pits |  |  |
| S’Chase:Drain the water jump |  |  |
| HT/DT: Check throws cage for damage and report if necessary |  |  |
| LJ/TJ: Store competition boards & replace with blanking boards |  |  |
| Remove equipment and hurdles to storage. |  |  |

# Text boxes

Athletics Facility Competition Checklist		Name of Facility:      			Event: 				Date of event:  ____

Xxxxxxxxxx xxxxxxxxxx xxxxxxxxxxx xxxxxxx x

Name:							Signature:						Date:

Comments/Actions:

Athletics Facility Competition Checklist		Name of Facility:      			Event: 				Date of event:  ____

Xxxxxxxxxx xxxxxxxxxx xxxxxxxxxxx xxxxxxx x

Name:							Signature:						Date:

Comments/Actions: